## Slide 1: Bluetooth Basics
Bluetooth
  Short-range radio frequency (RF) transmissions
  Rapid ad-hoc, “on-the-fly” device pairings
    Example: smartphone and a Bluetooth mouse
  Personal Area Network (PAN) technology
Two types of Bluetooth network topologies
  Piconet
  Scatternet
Notes: Bluetooth Attacks
Bluetooth
  Wireless technology that uses short-range radio frequency (RF) transmissions
  Provides rapid ad-hoc, “on-the-fly” device pairings
    Example: smartphone and a Bluetooth mouse
  Personal Area Network (PAN) technology
Two types of Bluetooth network topologies
  Piconet
  Scatternet

## Slide 2: Bluetooth Basics
Notes: Bluetooth Attacks
Table 9-1 Bluetooth products

## Slide 3: Bluetooth Basics
Piconet
  Established when two Bluetooth devices come within range of each other
  One device (master) controls the wireless communication
  Other device (slave) takes commands
    Active slaves are sending transmissions
    Parked slaves are connected but not actively participating
Notes: Bluetooth Attacks
Piconet
  Established when two Bluetooth devices come within range of each other
  One device (master) controls all wireless traffic
  Other device (slave) takes commands
    Active slaves are sending transmissions
    Parked slaves are connected but not actively participating

## Slide 4: Bluetooth Basics
Notes: Bluetooth Attacks
Figure 9-1 Bluetooth piconet

## Slide 5: Bluetooth Basics
Scatternet
  Group of piconets with connections between different piconets
Notes: Bluetooth Attacks
Scatternet
  Group of piconets with connections between different piconets
Figure 9-2 Bluetooth scatternet

## Slide 6: Bluetooth Attacks
Bluejacking - attacker sends unsolicited messages to Bluetooth-enabled devices
  Text messages, images, or sounds
Considered more annoying than harmful
  No data is stolen
Notes: Bluetooth Attacks
Bluejacking - an attack that sends unsolicited messages to Bluetooth-enabled devices
  Text messages, images, or sounds
Bluejacking is considered more annoying than harmful
  No data is stolen

## Slide 7: Bluetooth Attacks
Bluesnarfing
  Attack that accesses unauthorized information from a wireless device through a Bluetooth connection
  Takes advantage of unprotected devices
    They don’t require permission before pairing
  Often between cell phones and laptops
  Attacker can access e-mails, contacts, or other data by connecting to the Bluetooth device without owner’s knowledge
Notes: Bluetooth Attacks
Bluesnarfing
  An attack that accesses unauthorized information from a wireless device through a Bluetooth connection
  Often between cell phones and laptops
  Attacker copies e-mails, contacts, or other data by connecting to the Bluetooth device without owner’s knowledge

## Slide 8: Near Field Communication (NFC) Attacks
Near field communication (NFC)
  Set of standards primarily for smartphones and smart cards
  VERY short range (few centimeters)
  Can be used to establish communication between devices in close proximity
NFC devices are used in contactless payment systems
  A consumer can pay for a purchase by simply tapping a store’s payment terminal with their smartphone
Notes: End class 10/24 1 PM
Near Field Communication (NFC) Attacks
Near field communication (NFC)
  A set of standards primarily for smartphones and smart cards that can be used to establish communication between devices in close proximity
NFC devices are used in contactless payment systems
  A consumer can pay for a purchase by simply tapping a store’s payment terminal with their smartphone

## Slide 9: Near Field Communication (NFC) Attacks
Notes: Near Field Communication (NFC) Attacks
Table 9-2 NFC risks and defenses

## Slide 10: WLAN Attacks
(IEEE) WLANS
1997: release of IEEE 802.11
  Standard for wireless local area networks (WLANs)
  Higher speeds added in 1999: IEEE 802.11b
Notes: End of class 10/14 10 AM 11 AM
WLAN Attacks
Institute of Electrical and Electronics Engineers (IEEE) WLANS
  Most influential organization for computer networking and wireless communications
  Dates back to 1884
  Began developing network architecture standards in the 1980s
1997: release of IEEE 802.11
  Standard for wireless local area networks (WLANs)
  Higher speeds added in 1999: IEEE 802.11b

## Slide 11: WLAN Attacks
IEEE 802.11a
  Specifies maximum rated speed of 54Mbps using the 5GHz spectrum
IEEE 802.11g
  Preserves stable and widely accepted features of 802.11b and increases data transfer rates similar to 802.11a
IEEE 802.11n
  Ratified in 2009
  Improvements: speed, coverage area, resistance to interference, and strong security
Notes: WLAN Attacks
IEEE 802.11a
  Specifies maximum rated speed of 54Mbps using the 5GHz spectrum
IEEE 802.11g
  Preserves stable and widely accepted features of 802.11b and increases data transfer rates similar to 802.11a
IEEE 802.11n
  Ratified in 2009
  Improvements: speed, coverage area, resistance to interference, and strong security

## Slide 12: WLAN Attacks
IEEE 802.11ac
  Ratified in early 2014 and has data rates over 7 Gbps
Notes: WLAN Attacks
IEEE 802.11ac
  Ratified in early 2014 and has data rates over 7 Gbps
Table 9-3 IEEE WLAN standards

## Slide 13: WLAN Attacks
WLAN Hardware
  Wireless network interface card adapter
    Same functions as wired adapter
    Antenna sends and receives signals
  Access point (AP) major parts
    Antenna and radio transmitter/receiver send/receive wireless signals
    Bridging software to interface wireless devices to other devices
    Wired network interface connects by cable to standard wired network
Notes: End of class 3/8/17
WLAN Attacks
WLAN Hardware
  Wireless client network interface card adapter
    Performs same functions as wired adapter
    Antenna sends and receives signals
  Access point (AP) major parts
    Antenna and radio transmitter/receiver send and receive wireless signals
    Bridging software to interface wireless devices to other devices
    Wired network interface allows it to connect by cable to standard wired network

## Slide 14: WLAN Attacks
WLAN Hardware (cont’d)
  Access point (AP) functions
    Acts as “base station” for wireless devices
    A bridge between wireless and wired networks
      Can connect to wired network by a cable
  Wireless broadband routers
    Single hardware device containing AP, firewall, router, and DHCP server
    Also known as residential WLAN gateways
Notes: WLAN Attacks
WLAN Hardware (cont’d)
  Access point (AP) functions
    Acts as “base station” for wireless network
    Acts as a bridge between wireless and wired networks
      Can connect to wired network by a cable
  Wireless broadband routers
    Single hardware device containing AP, firewall, router, and DHCP server
    Also known as residential WLAN gateways

## Slide 15: WLAN Attacks
Notes: WLAN Attacks
Figure 9-4 Access point (AP) in WLAN

## Slide 16: WLAN Attacks
In a wired network, a well-defined boundary protects data and resources
  Boundary is known as a “hard edge”
WLANs in enterprises creates “blurred edges”
Types of wireless attacks
  Rogue access points
  Evil twins
  Intercepting wireless data
  Wireless replay attacks and denial of service attacks
Notes: WLAN Attacks
In a network, a well-defined boundary protects data and resources
  Boundary is known as a “hard edge”
The introduction of WLANs in enterprises has changed hard edges to “blurred edges”
Types of wireless attacks
  Rogue access points
  Evil twins
  Intercepting wireless data
  Wireless replay attacks and denial of service attacks

## Slide 17: WLAN Attacks
Rogue access point
  An unauthorized access point –
    allows attacker to bypass network security configurations
  Usually set up by insider (employee)
  May be behind firewall
Evil twin
  AP set up by attacker
  Attempts to mimic an authorized AP (same SSID)
  Attackers capture transmissions from users to evil twin AP
Notes: WLAN Attacks
Rogue access point
  An unauthorized access point that allows an attacker to bypass network security configurations
  Usually set up by an insider (employee)
  May be set up behind a firewall, opening the network to attacks
Evil twin
  AP set up by an attacker
  Attempts to mimic an authorized AP
  Attackers capture transmissions from users to evil twin AP

## Slide 18: WLAN Attacks
Notes: WLAN Attacks
Figure 9-7 Rogue access point and evil twin attacks

## Slide 19: WLAN Attacks
Intercepting Wireless Data
  Network interface card (NIC) adapter in promiscuous mode
  Wireless traffic captured
    packet read using a protocol analyzer
  A wireless NIC in monitor mode can capture frames without being associated with an AP
Notes: WLAN Attacks
Intercepting Wireless Data
  Wireless traffic captured to decode and analyze packet contents by using a protocol analyzer
  Network interface card (NIC) adapter must be in the correct mode in order for data to be captured
It is necessary for the wireless NIC to operate in monitor mode so that it can capture frames without first being associated with an AP
  Monitor mode is also called RF Monitor or RFMON

## Slide 20: WLAN Attacks
Wireless Replay Attack
  Also known as “hijacking”
  Passive attack, the attacker:
    captures transmitted wireless data records
    sends on to the original recipient without the attacker’s presence being detected
  Can be accomplished using an evil twin AP
Notes: WLAN Attacks
Wireless Replay Attack
  Also known as “hijacking”
  A passive attack in which the attacker captures transmitted wireless data, records it, and then sends it on to the original recipient without the attacker’s presence being detected
  Can be accomplished using an evil twin AP

## Slide 21: WLAN Attacks
Wireless Denial of Service Attack
  Jamming - attackers flood the RF spectrum with enough interference to prevent device-to-AP communication
  Spoofing - attackers create fictitious frame pretends to be from trusted client
  Manipulating duration field values - attackers send a frame with high duration field, preventing other devices from transmitting for that period of time
Notes: WLAN Attacks
Wireless Denial of Service Attack
  RF jamming - attackers use intentional RF interference to flood the RF spectrum with enough interference to prevent a device from communicating with the AP
  Spoofing - attackers craft a fictitious frame that pretends to come from a trusted client when it actually comes from the attacker
  Manipulating duration field values - attackers send a frame with the duration field set to a high value, preventing other devices from transmitting for that period of time

## Slide 22: WLAN Attacks
Wireless Home Attacks –
  most home users fail to configure any security on home networks
Attackers can:
  Steal data
  Read wireless transmissions
  Inject malware
  Download harmful content
War driving
  Search for wireless signals from an automobile or on foot using a portable computing device
Notes: WLAN Attacks
Wireless Home Attacks - most home users fail to configure any security on their home networks
Attackers can:
  Steal data
  Read wireless transmissions
  Inject malware
  Download harmful content
War driving
  Searching for wireless signals from an automobile or on foot using a portable computing device

## Slide 23: WLAN Attacks
Notes: WLAN Attacks
Table 9-4 War driving tools

## Slide 24: WLAN Attacks
War chalking
  Documenting / advertising location of wireless LANs for others to use
  Previously location marked drawing on sidewalks/walls
  Today, locations are posted on Web sites
Notes: WLAN Attacks
War chalking
  Documenting and then advertising location of wireless LANs for others to use
  Previously done by drawing on sidewalks or walls around network area
  Today, locations are posted on Web sites
Figure 9-8 War chalking symbols

## Slide 25: Vulnerabilities of IEEE 802.11 Security
Original IEEE 802.11 committee recognized wireless transmissions could be vulnerable
  Implemented several wireless security protections in the standard
  Left others to WLAN vendor’s discretion
  Protections were vulnerable and led to multiple attacks
Notes: End of class 3/10/17
Vulnerabilities of IEEE 802.11 Security
Original IEEE 802.11 committee recognized wireless transmissions could be vulnerable
  Implemented several wireless security protections in the standard
  Left others to WLAN vendor’s discretion
  Protections were vulnerable and led to multiple attacks

## Slide 26: Wired Equivalent Privacy (WEP)
IEEE 802.11 security protocol
  designed to ensure that only authorized parties can view transmissions
  Encrypts messages
Secret key shared between all clients and AP
WEP vulnerabilities
  Only 64-bit or 128-bit number to encrypt
    Initialization vector (IV) is only 24 of those bits
    Short length makes it easier to break - repeats quickly
Notes: Wired Equivalent Privacy (WEP)
IEEE 802.11 security protocol designed to ensure that only authorized parties can view transmissions
  Encrypts plaintext into ciphertext
Secret key is shared between wireless client device and AP
WEP vulnerabilities
  WEP can only use 64-bit or 128-bit number to encrypt
    Initialization vector (IV) is only 24 of those bits
    Short length makes it easier to break

## Slide 27: WEP - Shared Key Authentication
All clients use the same authentication key
Session initiated with a 4-way handshake.

## Slide 28: WEP - Encryption
Encrypts plaintext to ciphertext
Secret key shared between wireless client and AP
  entered on devices before transmission.
CRC: cyclic redundancy check
ICV: integrity check value
PRNG=>pseudo random number generator (up to 128 bits)

## Slide 29: WEP – Encryption (cont’d.)
WEP vulnerabilities
  64-bit or 128-bit number to encrypt
    Initialization vector (IV) only 24 of those bits
    Short = it easy to break
  Eventually, Init Vectors start repeating
    24 bits  16,777,216 possible values
    AP transmitting at 11 Mbps  700 packets per second
    Different IV per packet, IVs repeat
Key stream attack (or IV attack)
  Given how WEP works, an XOR on two ciphertexts = an XOR on two plaintexts
  If one plaintext known, the other can be computed.

## Slide 30
Packet 1 and 222 have same IV
Attacker knows plaintext 1
XOR ciphertexts
XOR result with KNOWN plaintext 1
Produces unknown plaintext 222

## Slide 31: Wired Equivalent Privacy (WEP)
WEP vulnerabilities (cont’d.)
  Violates cardinal rule of cryptography: avoid a detectable pattern
    Attackers can see duplication when IVs start repeating
Notes: Wired Equivalent Privacy (WEP)
WEP vulnerabilities (cont’d.)
  Violates cardinal rule of cryptography: avoid a detectable pattern
    Attackers can see duplication when IVs start repeating

## Slide 32: Wi-Fi Protected Setup (WPS)
WPS provides an optional means of configuring security on WLANS (2007)
Two common WPS methods:
  PIN method –PIN printed on a sticker of the wireless router or displayed via software wizard
    User enters Pin and security configuration automatically occurs
  Push-button method - user pushes buttons and security configuration takes place
Notes: Wi-Fi Protected Setup (WPS)
WPS is an optional means of configuring security on WLANS
Two common WPS methods:
  PIN method - utilizes a PIN printed on a sticker of the wireless router or displayed through a software wizard
    User enters Pin and security configuration automatically occurs
  Push-button method - user pushes buttons and security configuration takes place

## Slide 33: Wi-Fi Protected Setup (WPS)
Design and implementation flaws:
  No lockout limit for entering PINs
  PIN is very short (8 characters)
  Last PIN character is only a checksum
  Wireless router reports the validity of the first and second halves of the PIN separately
    Allows attacker to identify each half independently! (much faster)
Notes: Wi-Fi Protected Setup (WPS)
Design and implementation flaws:
  There is no lockout limit for entering PINs
  The last PIN character is only a checksum
  The wireless router reports the validity of the first and second halves of the PIN separately

## Slide 34: MAC Address Filtering
Method of controlling WLAN access
  Limit a device’s access to AP
Media Access Control (MAC) address filtering
  Used by nearly all wireless AP vendors
  Permits or blocks device based on MAC address
Vulnerabilities of MAC address filtering
  Addresses exchanged in unencrypted format
    Attacker can see MAC of approved device and spoof it
  Managing large number of addresses is challenging
Notes: MAC Address Filtering
Method of controlling WLAN access
  Limit a device’s access to AP
Media Access Control (MAC) address filtering
  Used by nearly all wireless AP vendors
  Permits or blocks device based on MAC address
Vulnerabilities of MAC address filtering
  Addresses exchanged in unencrypted format
    Attacker can see address of approved device and substitute it on his own device
  Managing large number of addresses is challenging

## Slide 35: MAC Address Filtering
Notes: MAC Address Filtering
Figure 9-10 MAC address filtering

## Slide 36: Disabling SSID Broadcasts
Each device must be authenticated prior to connecting to the WLAN
Service Set Identifier (SSID)
  The user-supplied network name of a wireless network;
  default is to broadcast SSID so that devices can see it
    The broadcast can be restricted
Some wireless security sources encourage users to configure their APs to prevent the broadcast of the SSID
Notes: Disabling SSID Broadcasts
Each device must be authenticated prior to connecting to the WLAN
Service Set Identifier (SSID)
  The user-supplied network name of a wireless network; usually broadcast so that any device can see it
    The broadcast can be restricted
Some wireless security sources encourage users to configure their APs to prevent the broadcast of the SSID

## Slide 37: Disabling SSID Broadcasts
Not advertising SSID provides a weak degree of security and has limitations:
  SSID transmitted in other frames
  May prevent users roaming from one AP coverage area to another
  Not always possible to turn off SSID beaconing
Notes: Disabling SSID Broadcasts
Not advertising the SSID only provides a weak degree of security and has limitations:
  SSID can be discovered when transmitted in other frames
  May prevent users from being able to freely roam from one AP coverage area to another
  It’s not always possible to turn off SSID beaconing

## Slide 38: Wireless Security Solutions
A unified approach to WLAN security was needed
  IEEE and Wi-Fi Alliance developed security solutions
Resulting standards used today
  IEEE 802.11i
  WPA and WPA2
Notes: Wireless Security Solutions
A unified approach to WLAN security was needed
  IEEE and Wi-Fi Alliance began developing security solutions
Resulting standards used today
  IEEE 802.11i
  WPA and WPA2

## Slide 39: Wi-Fi Protected Access (WPA)
Introduced in 2003 by the Wi-Fi Alliance
A subset of IEEE 802.11i
Goal: protect present and future wireless devices
Temporal Key Integrity Protocol (TKIP) Encryption
  Used in WPA
  Uses a longer 128 bit key than WEP
  Dynamically generated for each new packet
  Includes a Message Integrity Check (MIC), designed to prevent man-in-the-middle attacks
Notes: Wi-Fi Protected Access (WPA)
Introduced in 2003 by the Wi-Fi Alliance
A subset of IEEE 802.11i
Design goal: protect present and future wireless devices
Temporal Key Integrity Protocol (TKIP) Encryption
  Used in WPA
  Uses a longer 128 bit key than WEP
  Dynamically generated for each new packet
  Includes a Message Integrity Check (MIC), designed to prevent man-in-the-middle attacks

## Slide 40: Wi-Fi Protected Access (WPA)
Pre-shared Key (PSK) Authentication
  After AP configured, client device must have same key value entered
  Key shared prior to communication taking place
  Uses a passphrase to generate encryption key
    Entered on each AP and wireless device in advance
  Not used for encryption
    Serves as starting point for mathematically generating encryption keys
Notes: 10 AM 10/26 11 AM
Wi-Fi Protected Access (WPA)
Preshared Key (PSK) Authentication
  After AP configured, client device must have same key value entered
  Key is shared prior to communication taking place
  Uses a passphrase to generate encryption key
    Must be entered on each AP and wireless device in advance
  Not used for encryption
    Serves as starting point for mathematically generating the encryption keys

## Slide 41: Wi-Fi Protected Access (WPA)
WPA Vulnerabilities
  Key management
    Key sharing is done manually w/o security protection
    Keys must be changed on a regular basis
    Keys must be disclosed to guest users and updated
  Passphrases
    passphrases of fewer than 20 characters subject to cracking
Notes: Wi-Fi Protected Access (WPA)
WPA Vulnerabilities
  Key management
    Key sharing is done manually without security protection
    Keys must be changed on a regular basis
    Key must be disclosed to guest users
  Passphrases
    PSK passphrases of fewer than 20 characters subject to cracking

## Slide 42: Wi-Fi Protected Access 2 (WPA2)
  Second generation of WPA is known as WPA2
  Introduced in 2004
  Based on final 802.11i standard
AES-CCMP Encryption
  Advanced Encryption Standard (AES) block cipher
  AES performs three steps on every block (128 bits) of plaintext
    13 rounds Bytes are substituted and rearranged
Notes: Wi-Fi Protected Access 2 (WPA2)
  Second generation of WPA is known as WPA2
  Introduced in 2004
  Based on final IEEE 802.11i standard
  Allows wireless clients using TKIP to operate in the same WLAN
AES-CCMP Encryption
  Advanced Encryption Standard (AES) block cipher
  AES performs three steps on every block (128 bits) of plaintext
    Within second step, multiple iterations are performed
    Bytes are substituted and rearranged

## Slide 43: Wi-Fi Protected Access 2 (WPA2)
AES-CCMP Encryption (cont’d)
  Encryption protocol used for WPA2
    Specifies the use of CCM with AES
  The Cipher Block Chaining Message Authentication Code (CBC-MAC) component of CCMP provides data integrity and authentication
  Both CCMP and TKIP use 128-bit key for encryption
    Both methods use a 64-bit message integrity check (MIC) value
Notes: Wi-Fi Protected Access 2 (WPA2)
AES-CCMP Encryption (cont’d)
  Counter Mode with Cipher Block Chaining Message Authentication Code Protocol (CCMP) is the encryption protocol used for WPA2
    Specifies the use of CCM with AES
  The Cipher Block Chaining Message Authentication Code (CBC-MAC) component of CCMP provides data integrity and authentication
  Both CCMP and TKIP use a 128-bit key for encryption
    Both methods use a 64-bit MIC value

## Slide 44: Wi-Fi Protected Access 2 (WPA2)
IEEE 802.1x authentication
  Originally developed for wired networks
  Provides greater degree of security by implementing port-based authentication
  Blocks all traffic on a port-by-port basis until client is authenticated
Notes: Wi-Fi Protected Access 2 (WPA2)
IEEE 802.1x authentication
  Originally developed for wired networks
  Provides greater degree of security by implementing port-based authentication
  Blocks all traffic on a port-by-port basis until client is authenticated

## Slide 45: Wi-Fi Protected Access 2 (WPA2)
Extensible Authentication Protocol (EAP)
  A framework for transporting authentication protocols
    Allows new protocols to be implemented!!!
  Defines message format
  Uses four types of packets
    Request
    Response
    Success
    Failure
Notes: Wi-Fi Protected Access 2 (WPA2)
Extensible Authentication Protocol (EAP)
  Created as a more secure alternative than CHAP and PAP
  A framework for transporting authentication protocols
  Defines message format
  Uses four types of packets
    Request
    Response
    Success
    Failure

## Slide 46: Wi-Fi Protected Access 2 (WPA2)
Two common EAP protocols:
  Lightweight EAP (LEAP)
    Proprietary method developed by Cisco Systems
    Requires mutual authentication
      used for WLAN encryption in Cisco client software
    Vulnerable to specific types of attacks
      No longer recommended by Cisco
  Protected EAP (PEAP)
    Simplifies deployment of 802.1x by using Microsoft Windows logins and passwords
    Creates encrypted channel between client and authentication server
Notes: Wi-Fi Protected Access 2 (WPA2)
Two common EAP protocols:
  Lightweight EAP (LEAP)
    A proprietary method developed by Cisco Systems
    Requires mutual authentication used for WLAN encryption using Cisco client software
    Can be vulnerable to specific types of attacks
      No longer recommended by Cisco
  Protected EAP (PEAP)
    Simplifies deployment of 802.1x by using Microsoft Windows logins and passwords
    Creates encrypted channel between client and authentication server

## Slide 47: Wi-Fi Protected Access 2 (WPA2)
Notes: Wi-Fi Protected Access 2 (WPA2)
Table 9-5 EAP protocols supported by WPA2 Enterprise

## Slide 48: Additional Wireless Security Protections
Captive Portal APs
  Uses a standard web browser to provide information
  Gives the wireless user the opportunity to agree to a policy or present valid login credentials
  ie: hotel authentication portal
Rogue AP Discovery Tools - 4 types of wireless probes can monitor airwaves for traffic:
  Wireless device probe - laptop
  Desktop probe
  Access point probe - built into AP
  Dedicated probe
Notes: Additional Wireless Security Protections
Captive Portal APs
  Uses a standard web browser to provide information
  Gives the wireless user the opportunity to agree to a policy or present valid login credentials
Rouge AP Discovery Tools - 4 types of wireless probes can monitor airwaves for traffic:
  Wireless device probe
  Desktop probe
  Access point probe
  Dedicated probe

## Slide 49: Additional Wireless Security Protections
Power level controls
  Some APs allow adjustment of the power level at which the LAN transmits
  Reducing power allows less signal to reach outsiders
  Reduces interference between APs
Antennas
  AP should be located near center of coverage area
  Place high on a wall to reduce signal obstructions and deter theft
Notes: Additional Wireless Security Protections
Power level controls
  Some APs allow adjustment of the power level at which the LAN transmits
  Reducing power allows less signal to reach outsiders
Antennas
  AP should be located near center of coverage area
  Place high on a wall to reduce signal obstructions and deter theft

## Slide 50: Additional Wireless Security Protections
Site Surveys
  An in-depth examination and analysis of a wireless LAN site
  Reasons for conducting a site survey
    Achieving the best possible performance from the WLAN
    Determining the best location for APs
    Ensuring coverage area will fulfill the organization’s requirements
    Map existing radio interference
    Enhance the security of a WLAN
Notes: Additional Wireless Security Protections
Site Surveys
  An in-depth examination and analysis of a wireless LAN site
  Reasons for conducting a site survey
    Achieving the best possible performance from the WLAN
    Determining the best location for APs
    Ensuring coverage area will fulfill the organization’s requirements
    Map existing radio interference
    Enhance the security of a WLAN