## Slide 1: Security Through Network Devices
Layered security
  Multiple types of security devices to protect a network
  Also called defense in depth
Layered security makes it more difficult for attacker
  Must have tools, knowledge, and skills to break through EACH layer
Achieved by using networking devices or hardware designed for security
Notes: Security Through Network Devices
Layered security
  A defense that uses multiple types of security devices to protect a network
  Also called defense in depth
A network with layered security will make it more difficult for an attacker
  He must have all the tools, knowledge, and skills to break through the various layers
Layered network security can be achieved by using networking devices or hardware designed for security

## Slide 2: Standard Network Devices
Security features found in network hardware
  Provide basic level of security
Network devices classified based on their function in the OSI model
  Standard released in 1978, revised in 1983, still used today
  Defines how networks prepares data for delivery and how data is handled once received
Notes: Standard Network Devices
Security features found in network hardware
  Provide basic level of security
Network devices can classified based on their function in the OSI model
  Standards released in 1978, revised in 1983, still used today
  Illustrates how a network prepares data for delivery and how data is handled once received

## Slide 3: Standard Network Devices
OSI model breaks networking steps into seven (or 5) layers
  Each layer has different networking tasks
  Cooperates with adjacent layers
Standard network devices classified by the OSI layer at which they function
Some devices include:
  Switches, routers, load balancers, and proxies
Notes: Standard Network Devices
OSI model breaks networking steps into seven layers
  Each layer has different networking tasks
  Each layer cooperates with adjacent layers
Standard network devices can be classified by the OSI layer at which they function
Some devices include:
  Switches, routers, load balancers, and proxies

## Slide 4: Standard Network Devices
Notes: Standard Network Devices
Table 7-1 OSI references model

## Slide 5: Standard Network Devices
Switches
  A device that connects network devices together
  Operates at Data Link Layer (Layer 2)
  Can determine which device is connected to each port
  Forward frames sent to that specific device (unicast) or frames sent to all devices (broadcast)
  Uses MAC addresses to identify devices
Notes: Standard Network Devices
Switches
  A network switch is a device that connects network devices together
  Operates at Data Link Layer (Layer 2)
  Can determine which device is connected to each port
  Can forward frames sent to that specific device (unicast) or frames sent to all devices (broadcast)
  Uses MAC addresses to identify devices

## Slide 6: Standard Network Devices
Switches (cont’d)
  An attacker attached to a switch will see only frames that are directed to that device and not others
  Earlier networks used hubs to connect devices to network
    Repeated all frames to all attached network devices
  Attackers could use protocol analyzer to capture all packets
    Could decode and analyze packet contents
Notes: Standard Network Devices
Switches (cont’d)
  An attacker attached to a switch will see only frames that are directed to that device and not others
  Earlier networks used hubs to connect devices to a network
    Hubs repeated all frames to all attached network devices
  Attackers could use a protocol analyzer to capture all packets
    Protocol analyzers could decode and analyze packet contents

## Slide 7: Standard Network Devices
Admin should be able to monitor network traffic
  Helps identify and troubleshoot network problems
Traffic monitoring methods
  Port mirroring
    Administrator configures the switch to copy traffic from some or all ports to a monitoring port on the switch
  Network tap (test access point)
    Separate device installed between two devices
Notes: Standard Network Devices
Network administrators should be able to monitor network traffic
  Helps identify and troubleshoot network problems
Traffic monitoring methods
  Port mirroring
    Allows administrator to configure the switch to copy traffic that occurs on some or all ports to a designated monitoring port on the switch
  Network tap (test access point)
    Separate device installed between two network devices

## Slide 8: Standard Network Devices
Notes: Standard Network Devices
Figure 7-1 Port mirroring

## Slide 9: Standard Network Devices
Notes: Standard Network Devices
Figure 7-2 Network tap

## Slide 10: Standard Network Devices
Notes: End of class 2/20/17
11 AM
Standard Network Devices
Table 7-2 Protecting the switch

## Slide 11: Standard Network Devices
Routers
  Forward packets across different computer networks
  Operate at Network Layer (Layer 3)
  Can be set to filter specific types of network traffic
Load balancers
  Help evenly distribute work across a network
  Allocate requests among multiple devices
Notes: Standard Network Devices
Routers
  Forward packets across different computer networks
  Operate at Network Layer (Layer 3)
  Can be set to filter out specific types of network traffic
Load balancers
  Help evenly distribute work across a network
  Allocate requests among multiple devices

## Slide 12: Standard Network Devices
Advantages of load-balancing technology
  Reduces probability of overloading a single server
  Optimizes bandwidth of network computers
  Reduces network downtime
  Achieved through software or hardware device (load balancer)
Notes: Standard Network Devices
Advantages of load-balancing technology
  Reduces probability of overloading a single server
  Optimizes bandwidth of network computers
  Reduces network downtime
Load balancing is achieved through software or hardware device (load balancer)
Load balancers are grouped into two categories:
  Layer 4 load balancers - act upon data found in Network and Transport layer protocols
  Layer 7 load balancers - distribute requests based on data found in Application layer protocols

## Slide 13: Standard Network Devices
Security advantages of load balancing
  Detect and stop attacks directed at a server or app
  Detect and prevent (DoS) and protocol attacks
  Some can deny attackers info about the network
    Hide HTTP error pages
    Remove server id headers from HTTP responses
Notes: Standard Network Devices
Security advantages of load balancing
  Can detect and stop attacks directed at a server or application
  Can detect and prevent denial-of-service (DoS) and protocol attacks
  Some can deny attackers information about the network
    Hide HTTP error pages
    Remove server identification headers from HTTP responses

## Slide 14: Standard Network Devices
Proxies - there are several types of proxies used in computer networking
  Proxy server - a computer or an app program that intercepts requests from the internal network and processes request on behalf of the user
  App-aware proxy - a special proxy server that “knows” the application protocols that it supports
Notes: End of class 10 AM 2/20/17
Standard Network Devices
Proxies - there are several types of proxies used in computer networking
  Proxy server - a computer or an application program that intercepts user requests from the internal network and processes that request on behalf of the user
  Application-aware proxy - a special proxy server that “knows” the application protocols that it supports

## Slide 15: Standard Network Devices
Advantages of proxy servers:
  Increased speed
  Reduced costs
  Improved management
  Stronger security
Reverse proxy
  Does not serve clients
  Routes incoming requests to the correct server
Notes: Standard Network Devices
Advantages of proxy servers:
  Increased speed
  Reduced costs
  Improved management
  Stronger security
Reverse proxy
  Does not serve clients
  Routes incoming requests to the correct server

## Slide 16: Standard Network Devices
Notes: Standard Network Devices
Figure 7-3 Proxy server

## Slide 17: Network Security Hardware
Specifically designed security hardware devices
  Greater protection than standard networking devices
Network Firewalls
  Can be software-based or hardware-based
  Inspect packets and either accept or deny entry
  Hardware firewalls usually outside the network security perimeter
Notes: Network Security Hardware
Specifically designed security hardware devices
  Provide greater protection than standard networking devices
Network Firewalls
  Can be software-based or hardware-based
  Both types inspect packets and either accept or deny entry
  Hardware firewalls are usually located outside the network security perimeter

## Slide 18: Network Security Hardware
Methods of firewall packet filtering
  Stateless packet filtering
    Inspects incoming packet and permit or deny based on conditions set by administrator
  Stateful packet filtering
    Keeps a record of the state connections in/out of network
    Makes decisions based on the connection and conditions
Notes: Network Security Hardware
Methods of firewall packet filtering
  Stateless packet filtering
    Inspects incoming packet and permits or denies based on conditions set by administrator
  Stateful packet filtering
    Keeps a record of the state of a connection
    Makes decisions based on the connection and conditions

## Slide 19: Network Security Hardware
Firewall actions on a packet
  Allow (let packet pass through)
  Drop (prevent the packet from passing into the network and send no response to sender)
  Reject (prevent the packet from passing into the network but send a message to the sender)
Rule-based firewalls
  Use a set of individual instructions to control actions
Notes: Network Security Hardware
Firewall actions on a packet
  Allow (let packet pass through)
  Drop (prevent the packet from passing into the network and send no response to sender)
  Reject (prevent the packet from passing into the network but send a message to the sender)
Rule-based firewalls
  Use a set of individual instructions to control actions, called firewall rules
  Each rule is a separate instruction processed in sequence telling the firewall what action to take

## Slide 20: Network Security Hardware
Application-Aware Firewalls
  Sometimes called a next-generation firewall (NGFW)
  Operate at a higher level
    identify applications sending packets through firewall
    make decisions about actions to take
Web app firewall
  Special application-aware firewall that
    looks deeply into packets that carry HTTP traffic
  Can block specific sites or types of HTTP traffic
Notes: Network Security Hardware
Application-Aware Firewalls
  Sometimes called a next-generation firewall (NGFW)
  Operate at a higher level by identifying applications that send packets through the firewall and make decisions about actions to take
Web application firewall
  Special type of application-aware firewall that looks deeply into packets that carry HTTP traffic
  Can block specific sites or specific types of HTTP traffic

## Slide 21: Network Security Hardware
Spam filters
  Enterprise-wide spam filters
    block spam before it reaches the host
Email systems use two protocols
  Simple Mail Transfer Protocol (SMTP)
    Handles outgoing mail
  Post Office Protocol (POP)
    Handles incoming mail
Notes: Network Security Hardware
Spam filters
  Enterprise-wide spam filters block spam before it reaches the host
Email systems use two protocols
  Simple Mail Transfer Protocol (SMTP)
    Handles outgoing mail
  Post Office Protocol (POP)
    Handles incoming mail

## Slide 22: Network Security Hardware
Spam filters installed with the SMTP server
  Typically SMTP server listens on port 25
  Filter configured to listen on port 25
  Pass non-spam e-mail to SMTP server listening on another port
  This prevents SMTP server from notifying spammer of failed message delivery
Notes: Network Security Hardware
Spam filters installed with the SMTP server
  Filter configured to listen on port 25
  Pass non-spam e-mail to SMTP server listening on another port
  This method prevents SMTP server from notifying spammer of failed message delivery

## Slide 23: Network Security Hardware
Notes: Network Security Hardware
Figure 7-7 Spam filter with SMTP server

## Slide 24: Network Security Hardware
IF Spam filters installed on the POP3 server instead
  All spam passes through SMTP server and is delivered to user’s mailbox
  Results in increased costs
    Storage, transmission, backup, deletion
Third-party entity contracted to filter spam
  All email directed to third-party’s remote spam filter
  E-mail cleansed before being redirected to organization
Notes: End of class 10/10/16 11 AM
Network Security Hardware
Spam filters installed on the POP3 server
  All spam must first pass through SMTP server and be delivered to user’s mailbox
  Can result in increased costs
    Storage, transmission, backup, deletion
Third-party entity contracted to filter spam
  All email directed to third-party’s remote spam filter
  E-mail cleansed before being redirected to organization

## Slide 25: Network Security Hardware
Notes: 10AM End of class 10/10/16 Network Security Hardware
Figure 7-8 Spam filter on POP3 server

## Slide 26: Network Security Hardware
Virtual private network (VPN)
  enables authorized users to use unsecured public network as if it were a secure private network
  All data sent between remote device and network is encrypted
Types of VPNs
  Remote-access VPN - a user-to-LAN connection
  Site-to-site - multiple sites can connect to other sites over the Internet
Notes: End of class 10 AM 2/22/17
Network Security Hardware
Virtual private network (VPN) - enables authorized users to use an unsecured public network as if it were a secure private network
  All data transmitted between remote device and network is encrypted
Types of VPNs
  Remote-access VPN - a user-to-LAN connection
  Site-to-site - multiple sites can connect to other sites over the Internet

## Slide 27: Network Security Hardware
Endpoints
  The ends of the tunnel between VPN devices
  May be
    Software on local computer
    A VPN concentrator (hardware device)
    Integrated into another networking device
VPN concentrator - dedicated device that aggregates hundreds or thousands of VPN connections
Notes: End of class 2/22/17
Network Security Hardware
Endpoints
  The end of the tunnel between VPN devices
  Used in communicating VPN transmissions
  May be software on local computer, a VPN concentrator (hardware device), or integrated into another networking device
VPN concentrator - a dedicated hardware device that aggregates hundreds or thousands of VPN connections

## Slide 28: Network Security Hardware
Tunneling protocols enclose a packet within another packet -- used for VPN transmissions
IPsec has two “subprotocols” that are used in VPN:
  Encapsulated Security Payload (ESP)
  Authentication Header (AH)
A remote-access VPN generally uses either IPsec or the Layer 2 Tunneling Protocol (L2TP)
Notes: Network Security Hardware
Tunneling protocols enclose a packet within another packet and are used for VPN transmissions
IPsec has two “subprotocols” that are used in VPN:
  Encapsulated Security Payload (ESP)
  Authentication Header (AH)
A remote-access VPN generally uses either IPsec or the Layer 2 Tunneling Protocol (L2TP)

## Slide 29: Network Security Hardware
Internet Content Filters
  Monitor Internet traffic
  Block access to preselected Web sites and files
  Unapproved sites can be restricted based
    URL (URL filtering)
    matching keywords (content inspection)
Notes: Network Security Hardware
Internet Content Filters
  Monitor Internet traffic
  Block access to preselected Web sites and files
  Unapproved sites can be restricted based on the URL (URL filtering) or matching keywords (content inspection)

## Slide 30: Network Security Hardware
Web Security Gateways
  Can block malicious content in real time
  Block content through application level filtering
Examples of blocked Web traffic
  Adware, spyware
  Cookies
  Instant messengers
  P2P (peer to peer) file sharing
  Script exploits
  TCP/IP malicious code attacks
Notes: Network Security Hardware
Web Security Gateways
  Can block malicious content in real time
  Block content through application level filtering
Examples of blocked Web traffic
  Adware, spyware
  Cookies
  Instant messengers
  P2P (peer to peer) file sharing
  Script exploits
  TCP/IP malicious code attacks

## Slide 31: Network Security Hardware
Intrusion detection system (IDS)
  Detects attack as it occurs
  Use various methods for monitoring for attacks
  Can be installed on either local hosts or networks
  An extension of IDS is an intrusion prevention system (IPS)
Notes: Network Security Hardware
Intrusion detection system (IDS)
  Can detect attack as it occurs
  IDS systems use different methodologies for monitoring for attacks
  Can be installed on either local hosts or networks
  An extension of IDS is an intrusion prevention system (IPS)

## Slide 32: Network Security Hardware
Monitoring methodologies
  Anomaly-based monitoring
    Compares current behavior with baseline
  Signature-based monitoring
    Looks for well-known attack patterns
  Behavior-based monitoring
    Detects abnormal actions by processes or programs
    Alerts user who decides whether to block activity
  Heuristic monitoring
    Uses experience-based techniques
Notes: Network Security Hardware
Monitoring methodologies
  Anomaly-based monitoring
    Compares current detected behavior with baseline
  Signature-based monitoring
    Looks for well-known attack signature patterns
  Behavior-based monitoring
    Detects abnormal actions by processes or programs
    Alerts user who decides whether to allow or block activity
  Heuristic monitoring
    Uses experience-based techniques

## Slide 33: Network Security Hardware
Notes: Network Security Hardware
Table 7-4 Methodology comparisons to trap port scanning application

## Slide 34: Network Security Hardware
Two basic types of IDS exist
Host intrusion detection system (HIDS)
  A software-based app that detects attack as it occurs
  Installed on each system needing protection
  Monitors (for anomalous activitiy):
    System calls and file system access
    Can recognize unauthorized Registry modification
    Host input and output communications
Notes: Network Security Hardware
Types of IDS - two basic types if IDS exist
Host intrusion detection system (HIDS)
  A software-based application that can detect an attack as it occurs
  Installed on each system needing protection
  Monitors:
    System calls and file system access
    Can recognize unauthorized Registry modification
    Host input and output communications
      Detects anomalous activity

## Slide 35: Network Security Hardware
Disadvantages of HIDS
  Can’t monitor network traffic that does not reach local system
  All log data is stored locally
  Resource-intensive and can slow local systems
Notes: Network Security Hardware
Disadvantages of HIDS
  Cannot monitor network traffic that does not reach local system
  All log data is stored locally
  Resource-intensive and can slow system

## Slide 36: Network Security Hardware
Network intrusion detection system (NIDS)
  Watches for attacks on the network
  Sensors installed on firewalls and routers:
    Gather info and report to central device
  Passive NIDS will sound an alarm
  May use one or more of the evaluation techniques listed in Table 7-5 (see the following slide)
Notes: Network Security Hardware
Network intrusion detection system (NIDS)
  Watches for attacks on the network
  NIDS sensors installed on firewalls and routers:
    Gather information and report back to central device
  Passive NIDS will sound an alarm
  An NIDS may use one or more of the evaluation techniques listed in Table 7-5 (see the following slide)

## Slide 37: Network Security Hardware
Notes: Network Security Hardware
Table 7-5 NDIS evaluation techniques

## Slide 38: Network Security Hardware
Application-aware IDS
  A specialized IDS
  Uses “contextual knowledge” in real time
  It can know the version of the OS or which application is running
    AND what vulnerabilities are present in the systems being protected
Notes: Network Security Hardware
Application-aware IDS
  A specialized IDS
  Capable of using “contextual knowledge” in real time
  It can know the version of the OS or which application is running
    As well as what vulnerabilities are present in the systems being protected

## Slide 39: Network Security Hardware
Intrusion Prevention System (IPS)
  Similar to NIDS
  Monitors traffic & immediately blocks malicious attack
  Located “in line” on the firewall
  More quickly take action to block an attack
Application-aware IPS
  Knows which apps are running as well as the underlying OS
Notes: Network Security Hardware
Intrusion Prevention System (IPS)
  Monitors network traffic to immediately block a malicious attack
  Similar to NIDS
  NIPS is located “in line” on the firewall
  Allows the NIPS to more quickly take action to block an attack
Application-aware IPS
  Knows which applications are running as well as the underlying OS

## Slide 40: Network Security Hardware
Unified Threat Management (UTM) Security Appliances
  Network hardware that provides multiple security functions, such as:
    Antispam, antiphishing, antivirus, and antispyware
    Bandwidth optimization
    Content filtering
    Encryption
    Firewall
    Instant messaging control and web filtering
    Intrusion protection
Notes: End of class 11 AM 10/12/16 1 PM
Network Security Hardware
Unified Threat Management (UTM) Security Appliances
  Network hardware that provides multiple security functions, such as:
    Antispam, antiphishing, antivirus, and antispyware
    Bandwidth optimization
    Content filtering
    Encryption
    Firewall
    Instant messaging control and web filtering
    Intrusion protection

## Slide 41: Security Through Network Technologies
  Routers normally drop packets with private address
Network address translation (NAT)
  Allows private IP addresses to be used on public Internet
  Replaces private IP address with public address
Port address translation (PAT)
  Variation of NAT
    Outgoing packets given same IP address but different TCP port number
Notes: End of class 10 AM, 11 AM 2/27/17
Security Through Network Technologies
  Internet routers normally drop packet with a private address
Network address translation (NAT)
  Allows private IP addresses to be used on the public Internet
  Replaces private IP address with public address
Port address translation (PAT)
  Variation of NAT
    Outgoing packets given same IP address but different TCP port number

## Slide 42: Security Through Network Technologies
Notes: Security Through Network Technologies
Table 7-6 Private IP addresses

## Slide 43: Security Through Network Technologies
Advantage of NAT
  Masks IP addresses of internal devices
  Attacker can’t determine actual IP address of sender
Network Access Control (NAC)
  Examines current state of system or network device:
    Before allowing the network connection
  Device must meet set of criteria
    If not met, NAC allows connection to a “quarantine” network until deficiencies corrected
Notes: Security Through Network Technologies
Advantage of NAT
  Masks IP addresses of internal devices
  An attacker who captures the packet on the Internet cannot determine the actual IP address of sender
Network Access Control (NAC)
  Examines current state of system or network device:
    Before allowing the network connection
  Device must meet set of criteria
    If not met, NAC allows connection to a “quarantine” network until deficiencies corrected

## Slide 44: Security Through Network Technologies
Notes: Security Through Network Technologies
Figure 7-10 Network access control (NAC) framework

## Slide 45: Security Through Network Design Elements
Elements of a secure network design
  Demilitarized zones
  Subnetting
  Virtual LANs
  Remote access
Notes: End of class 10 AM 10/12/16
Security Through Network Design Elements
Elements of a secure network design
  Demilitarized zones
  Subnetting
  Virtual LANs
  Remote access

## Slide 46: Demilitarized Zone (DMZ)
DMZ - a separate network located outside secure network perimeter
Untrusted outside users can access resources within the DMZ but not the secure network
Notes: Demilitarized Zone (DMZ)
DMZ - a separate network located outside secure network perimeter
Untrusted outside users can access DMZ but not secure network

## Slide 47: Demilitarized Zone (DMZ)
Notes: Demilitarized Zone (DMZ)
Figure 7-11 DMZ with one firewall

## Slide 48: Demilitarized Zone (DMZ)
Notes: Demilitarized Zone (DMZ)
Figure 7-12 DMZ with two firewalls

## Slide 49: Subnetting
IP address is used to identify a network and a host on that network
  part of address is a network address
  The rest is a host address
Subnetting allows a large network to be divided into smaller subnets
Each network can contain several subnets
  Subnets connected through different routers
Subnet can contain multiple hosts
Notes: Subnetting
An IP address is used to identify a network and a host on that network
  One part is a network address and one part is a host address
Subnetting allows a large network to be divided into smaller subnets
Each network can contain several subnets
  Each subnet is connected through different routers
Each subnet can contain multiple hosts

## Slide 50: Subnetting
Better network security by isolating groups of hosts
Admins can utilize network security tools
  easier to regulate who has access in and out of a particular subnetwork
Allows admins to hide the internal network layout
  More difficult for attackers to target their attacks
  Obscurity!
Notes: Subnetting
Improves network security by isolating groups of hosts
Administrators can utilize network security tools to make it easier to regulate who has access in and out of a particular subnetwork
Allows network administrators to hide the internal network layout
  Makes it more difficult for attackers to target their attacks

## Slide 51: Subnetting
Notes: Subnetting
Table 7-7 Advantages of subnetting

## Slide 52: Virtual LANs (VLAN)
Scattered users are logically grouped together
  Even if attached to different switches
Can isolate sensitive data to VLAN members
Communication on a VLAN
  Connected to same switch, switch handles packet transfer
  Special “tagging” protocol is used for communicating between switches
Notes: Virtual LANs (VLAN)
Allow scattered users to be logically grouped together
  Even if attached to different switches
Can isolate sensitive data to VLAN members
Communication on a VLAN
  If connected to same switch, switch handles packet transfer
  A special “tagging” protocol is used for communicating between switches