## Slide 1: Common Network Protocols
Protocols
  Rules for communication
  Essential for proper comms between network devices
Transmission Control Protocol/Internet Protocol (TCP/IP)
  Most common protocol suite used for local area networks and the Internet
  Several protocols that all function together
Notes: Common Network Protocols
Protocols
  Rules for communication
  Essential for proper communication between network devices
Transmission Control Protocol/Internet Protocol (TCP/IP)
  Most common protocol suite used for local area networks and the Internet
  Comprises several protocols that all function together

## Slide 2: Common Network Protocols
IP
  Protocol that functions primarily at Open Systems Interconnection (OSI) Network Layer (Layer 3)
  Provides network addressing and routing
TCP
  Transport Layer (Layer 4) protocol
  Establishes connections and ensures reliable data transport between devices
TCP/IP uses a four layer architecture
  Network Interface, Internet, Transport, Application
Notes: Common Network Protocols
IP
  Protocol that functions primarily at Open Systems Interconnection (OSI) Network Layer (Layer 3)
  Provides network addressing and routing
TCP
  Transport Layer (Layer 4) protocol
  Establishes connections and ensures reliable data transport between devices
TCP/IP uses a four layer architecture
  Network Interface, Internet, Transport, Application

## Slide 3: Common Network Protocols
Several basic TCP/IP Protocols:
  Internet Control Message Protocol (ICMP)
  Simple Network Management Protocol (SNMP)
  Domain Name System (DNS)
  File transfer and storage protocols
  NetBIOS
  Telnet
A new and more secure version of IP is designed to replace the current version
Notes: Common Network Protocols
Several basic TCP/IP Protocols:
  Internet Control Message Protocol (ICMP)
  Simple Network Management Protocol (SNMP)
  Domain Name System (DNS)
  File transfer and storage protocols
  NetBIOS
  Telnet
A new and more secure version of IP is designed to replace the current version

## Slide 4: Internet Control Message Protocol (ICMP)
ICMP
  Used by devices to communicate updates or error information to other devices
  Messages are divided into two classes:
    Informational and query messages
    Error messages
Notes: Internet Control Message Protocol (ICMP)
ICMP
  Used by devices to communicate updates or error information to other devices
  ICMP messages are divided into two classes:
    Informational and query messages
    Error messages

## Slide 5: Internet Control Message Protocol (ICMP)
ICMP message fields
  Type
    Identifies general message category
  Code
    Gives additional information about the Type field
  Checksum
    Verifies message integrity
  Message Body
    Contains information about the specific ICMP message
Notes: Internet Control Message Protocol (ICMP)
ICMP message fields
  Type
    Identifies general message category
  Code
    Gives additional information about the Type field
  Checksum
    Verifies message integrity
  Message Body
    Contains information about the specific ICMP message

## Slide 6: Internet Control Message Protocol (ICMP)
Notes: Internet Control Message Protocol (ICMP)
Table 8-1 Common ICMP code values for Type 3, Destination Unreachable

## Slide 7: Internet Control Message Protocol (ICMP)
Attacks that that advantage of ICMP
  Network discovery
  Smurf attack
  ICMP redirect attack
  Ping of death
Notes: Internet Control Message Protocol (ICMP)
Attacks that that advantage of ICMP
  Network discovery
  Smurf attack
  ICMP redirect attack
  Ping of death

## Slide 8: Simple Network Management Protocol (SNMP)
Use: manage network equipment.
Supported by most equipment manufacturers
Allows admins to remotely monitor, manage, and configure devices
Functions by exchanging management information between network devices
Each SNMP-managed device has an agent or a service
  Listens for and executes commands
Notes: End of class 3/1/17
Simple Network Management Protocol (SNMP)
Used to manage network equipment and is supported by most network equipment manufacturers
Allows administrators to remotely monitor, manage, and configure network devices
Functions by exchanging management information between network devices
Each SNMP-managed device has an agent or a service
  Listens for and executes commands

## Slide 9: Simple Network Management Protocol (SNMP)
Agents are password protected
  Password is known as a community string
Security vulnerabilities were present in SMNP versions 1 and 2
  Community strings were transmitted as clear text!
  Version 3 uses usernames and passwords along with encryption to address vulnerabilities
Notes: Simple Network Management Protocol (SNMP)
Agents are password protected
  Password is known as a community string
Security vulnerabilities were present in SMNP versions 1 and 2
  Version 3 uses usernames and passwords along with encryption to address vulnerabilities

## Slide 10: Domain Name System (DNS)
TCP/IP protocol that maps IP addresses to their symbolic name
The DNS database is hierarchical
  Records contain the name of a site and a corresponding IP number
Distributed to many different servers on the Internet
  Prevent bottlenecking and ensure efficiency
Notes: Domain Name System (DNS)
A TCP/IP protocol that maps IP addresses to their symbolic name
The DNS database is organized as a hierarchy
  Database consists of the name of a site and a corresponding IP number
Database is distributed to many different servers on the Internet
  To prevent bottlenecking and to ensure efficiency

## Slide 11: Domain Name System (DNS)
Notes: Domain Name System (DNS)
Figure 8-2 DNS look up

## Slide 12: Domain Name System (DNS)
DNS is often the focus of attacks
  DNS poisoning substitutes fraudulent IP address
    Can be in local host table or external DNS server
    Newest DNS software prevents DNS poisoning
  Attacker asks the valid DNS for a zone transfer
    A zone transfer allows attacker access to network, hardware, and operating system information
Notes: Domain Name System (DNS)
DNS is often the focus of attacks
  DNS poisoning substitutes fraudulent IP address
    Can be done in local host table or external DNS server
    Latest edition of DNS software prevents DNS poisoning
  Attacker asks the valid DNS for a zone transfer
    A zone transfer allows attacker access to network, hardware, and operating system information

## Slide 13: File Transfer Protocols
TCP/IP protocols are used for transferring files
  File transfer protocol (FTP) - used to connect to an FTP “server”
Methods for using FTP on local host computer
  From a command prompt
  Using a web browser
  Using an FTP client
FTP uses two ports
  Port 21 is the FTP control part
  Port 20 is the data port
Notes: File Transfer Protocols
TCP/IP protocols are used for transferring files
  File transfer protocol (FTP) - used to connect to an FTP server
  Trivial file transfer protocol (TFTP) - a “light” version of FTP that uses a small amount of memory
Methods for using FTP on local host computer
  From a command prompt
  Using a web browser
  Using an FTP client

## Slide 14: File Transfer Protocols
Notes: 10/17/16 end of class 10 AM
File Transfer Protocols
Figure 8-3 FTP client

## Slide 15: File Transfer Protocols
FTP vulnerabilities
  Does not use encryption
  Vulnerable to man-in-the-middle attacks
Secure transmission options over FTP
  Secure sockets layer (FTPS) encrypts commands
    Uses SSL or TLS to encrypt commands sent over the control port (port 21); data port may not be encrypted
  Secure FTP (SFTP)
    Uses only a single TCP port instead of two ports
    All data and commands are encrypted
Notes: File Transfer Protocols
FTP vulnerabilities
  Does not use encryption
  Files transferred using FTP are vulnerable to man-in-the-middle attacks
Secure transmission options over FTP
  Secure sockets layer (FTPS) encrypts commands
    Uses SSL or TLS to encrypt commands sent over the control port (port 21); data port may not be encrypted
  Secure FTP (SFTP)
    Uses only a single TCP port instead of two ports
    All data and commands are encrypted

## Slide 16: File Transfer Protocols (cont’d.)
Secure Copy Protocol (SCP)
  An enhanced version of Remote Copy Protocol (RCP)
  Encrypts files and commands
  File transfer cannot be interrupted and then resumed in the same session
    Session must be completely terminated and restarted
  Found mainly on Linux and UNIX platforms
Notes: File Transfer Protocols (cont’d.)
Secure Copy Protocol (SCP)
  An enhanced version of Remote Copy Protocol (RCP)
  Encrypts files and commands
  File transfer cannot be interrupted and then resumed in the same session
    Session must be completely terminated and restarted
  Found mainly on Linux and UNIX platforms

## Slide 17: Storage Protocols
As storage capacities have grown, most organizations have turned to using a storage area network (SAN)
  A dedicated network storage facility that provides access to data storage over a high-speed network
iSCSI (Internet Small Computer System Interface) - an IP-based storage networking standard for linking data storage facilities
  Can transmit data over LANs, WANs, and the Internet
Notes: Storage Protocols
As storage capacities have grown, most organizations have turned to using a storage area network (SAN)
  A dedicated network storage facility that provides access to data storage over a high-speed network
iSCSI (Internet Small Computer System Interface) - an IP-based storage networking standard for linking data storage facilities
  Can transmit data over LANs, WANs, and the Internet

## Slide 18: Storage Protocols
Fibre Channel (FC) - a high-speed storage network protocol that can transmit up to 16 Gbps
Fibre Channel over Ethernet (FCoE)
  A variation of FC that encapsulates Fibre Channel frames over Ethernet networks
  Allows FC to use fast Ethernet networks while preserving the FC protocol
FC zones - a built-in security mechanism
  There are two types:
    FC hard zone - based on port number
    FC soft zone - based on device ID (cross-port)
Notes: End of class 10/19/16 11 AM 1PM
Storage Protocols
Fibre Channel (FC) - a high-speed storage network protocol that can transmit up to 16 Gbps
Fibre Channel over Ethernet (FCoE)
  A variation of FC that encapsulates Fibre Channel frames over Ethernet networks
  Allows FC to use fast Ethernet networks while preserving the FC protocol
FC zones - a built-in security mechanism
  There are two types:
    FC hard zone
    FC soft zone

## Slide 19: NetBIOS
NetBIOS (Network Basic Input/Output System)
  A transport protocol used by Microsoft Windows systems
  Allows applications on separate computers to communicate over a LAN
  An attacker who determines that NetBIOS is running can use an application to gather information regarding the network in order to design an attack
  It is recommended to disable NetBIOS or use only if necessary on specific devices that require it
Notes: NetBIOS
NetBIOS (Network Basic Input/Output System)
  A transport protocol used by Microsoft Windows systems
  Allows applications on separate computers to communicate over a LAN
  An attacker who determines that NetBIOS is running can use an application to gather information regarding the network in order to design an attack
  It is recommended to disable NetBIOS or used only if necessary on specific devices that require it

## Slide 20: Telnet
Telnet
  An older TCP/IP protocol for text-based communication
  Also a terminal emulation application that runs on a local computer
    Connects to a server on a network
  Telnet does not encrypt data and many security weaknesses have been uncovered within the protocol
  It is recommended that Secure Shell (SSH) be used instead of Telnet
Notes: Telnet
Telnet
  An older TCP/IP protocol for text-based communication
  Also a terminal emulation application that runs on a local computer
    Connects to a server on a network
  Telnet does not encrypt data and many security weaknesses have been uncovered within the protocol
  It is recommended that Secure Shell (SSH) be used instead of Telnet

## Slide 21: IPv6
Current version of IP protocol is version 4 (IPv4)
  Developed in 1981
  Number of available IP address is limited to 4.3 billion
    This is no longer sufficient for the number of devices that are connected to the Internet
  Has security weaknesses
Internet Protocol version 6 (IPv6)
  Next generation of IP protocol
  Addresses weaknesses of IPv4
Notes: IPv6
Current version of IP protocol is version 4 (IPv4)
  Developed in 1981
  Number of available IP address is limited to 4.3 billion
    This is no longer sufficient for the number of devices that are connected to the Internet
  Has security weaknesses
Internet Protocol version 6 (IPv6)
  Next generation of IP protocol
  Addresses weaknesses of IPv4

## Slide 22: IPv6
Notes: IPv6
Figure 8-5 IPv4 and IPv6 headers

## Slide 23: IPv6
IPv6 provides enhanced security features
  Cryptographic protocols provide secure data communication
  New authentication headers prevent IP packets from being altered
Notes: End of class 10 AM 3/3/17
IPv6
IPv6 provides enhanced security features
  Cryptographic protocols provide secure data communication
  New authentication headers prevent IP packets from being altered

## Slide 24: IPv6
Notes: IPv6
Table 8-3 Comparison of IPv4 and IPv6 headers

## Slide 25: Network Administration Principles
Administering a secure network can be challenging
Rule-based management approach
  Relies on following procedures and rules
  Procedural rules are the authoritative and prescribed direction for conduct
    Procedural rules dictate technical rules
  Technical rules address:
    Device security
    Monitoring and analyzing logs
    Network design management
    Port security
Notes: Network Administration Principles
Administering a secure network can be challenging
Rule-based management approach
  Relies on following procedures and rules
  Procedural rules are the authoritative and prescribed direction for conduct
    Procedural rules dictate technical rules
  Technical rules address:
    Device security
    Monitoring and analyzing logs
    Network design management
    Port security

## Slide 26: Device Security
Device security involves:
  Establishing a secure router configuration
  Implementing flood guards
Secure router configuration
  Router operates at Network Layer (Layer 3)
    Forwards packets across computer networks
  Routers can perform a security function
    Can be configured to filter out specific types of network traffic
Notes: Device Security
Device security involves:
  Establishing a secure router configuration
  Implementing flood guards
Secure router configuration
  Router operates at Network Layer (Layer 3)
    Forwards packets across computer networks
  Routers can perform a security function
    Can be configured to filter out specific types of network traffic

## Slide 27: Device Security
Notes: End of class 10/19/16 10 AM
Device Security
Table 8-4 Secure router configuration tasks

## Slide 28: Device Security
Flood guard
  Protects against denial of service (DoS) attacks
  SYN flood attack
    A type of DoS attack that takes advantage of the procedures for initiating a session
  A flood guard controls a device’s tolerance for unanswered service requests
    Administrator can set a maximum number of “developing” connections
  Commonly found on firewalls, IDSs, and IPSs
Notes: Device Security
Flood guard
  Protects against denial of service (DoS) attacks
  SYN flood attack
    A type of DoS attack that takes advantage of the procedures for initiating a session
  A flood guard controls a device’s tolerance for unanswered service requests
    Administrator can set a maximum number of “developing” connections
  Commonly found on firewalls, IDSs, and IPSs

## Slide 29: Monitoring and Analyzing Logs
Security logs
  Can reveal types of attacks that are being directed at the network and if attacks were successful
Access logs
  Provide details regarding requests for specific files
Audit logs
  Used to record which user performed an action
Event logs
  Document any unsuccessful events and the most significant successful events
Notes: Monitoring and Analyzing Logs
Security logs
  Can reveal types of attacks that are being directed at the network and if attacks were successful
Access logs
  Provide details regarding requests for specific files
Audit logs
  Used to record which user performed an action
Event logs
  Document any unsuccessful events and the most significant successful events

## Slide 30: Monitoring and Analyzing Logs
A routine review of logs helps to:
  Identify security incidents
  Policy violations
  Fraudulent activity
  Operational problems
Logs can be useful for:
  Performing auditing analysis
  Supporting the organization’s internal investigations
  Identifying operational trends and long-term problems
Notes: Monitoring and Analyzing Logs
A routine review of logs helps to:
  Identify security incidents
  Policy violations
  Fraudulent activity
  Operational problems
Logs can be useful for:
  Performing auditing analysis
  Supporting the organization’s internal investigations
  Identifying operational trends and long-term problems

## Slide 31: Monitoring and Analyzing Logs
Logs can provide documentation that the organization is complying with laws and regulatory requirements
Firewall log items to be examined
  IP addresses rejected and dropped
  Probes to ports that have no application services on them
  Source-routed packets
  Suspicious outbound connections
  Unsuccessful logins
Notes: Monitoring and Analyzing Logs
Logs can provide documentation that the organization is complying with laws and regulatory requirements
Firewall log items to be examined
  IP addresses rejected and dropped
  Probes to ports that have no application services on them
  Source-routed packets
  Suspicious outbound connections
  Unsuccessful logins

## Slide 32: Monitoring and Analyzing Logs
Notes: Monitoring and Analyzing Logs
Table 8-5 Device logs with beneficial security data

## Slide 33: Monitoring and Analyzing Logs
Problems with log management:
  Multiple devices generating logs
  Very large volumes of data
  Different log formats
A solution to log management is to use a centralized device log analyzer
Notes: Monitoring and Analyzing Logs
Problems with log management:
  Multiple devices generating logs
  Very large volumes of data
  Different log formats
A solution to log management is to use a centralized device log analyzer

## Slide 34: Network Design Management
Several network design management principles should be followed to ensure a secure network
Network separation
  Provides separation between different parts of the network
  Example: order entry network segment cannot access the network that controls heating and cooling
Option to accomplish network separation
  Physically separate users by connecting them to different switches and routers
Notes: 10/21 End of class 11 AM Network Design Management
Several network design management principles should be followed to ensure a secure network
Network separation
  Provides separation between different parts of the network
  Example: order entry network segment cannot access the network that controls heating and cooling
Option to accomplish network separation
  Physically separate users by connecting them to different switches and routers

## Slide 35: Network Design Management
Loop protection
  Refer to Figure 8-7 for a description of a broadcast storm
  Host Z wants to send frames to Host X
  Switch A floods network with the packet
  Packet travels down the network segments to the Switches B and C
  Switches B and C add Host Z to their lookup tables
  Both switches flood Segment 2 looking for Host X
    They receive each other’s packets and flood them back out again
Notes: Network Design Management
Loop protection
  Refer to Figure 8-7 for a description of a broadcast storm
  Host Z wants to send frames to Host X
  Switch A floods network with the packet
  Packet travels down the network segments to the Switches B and C
  Switches B and C add Host Z to their lookup tables
  Both switches flood Segment 2 looking for Host X
    They receive each other’s packets and flood them back out again

## Slide 36: Network Design Management
Notes: Network Design Management
Figure 8-7 Broadcast storm

## Slide 37: Network Design Management
Loop protection can prevent broadcast storms
  Uses IEEE 802.1d spanning tree algorithm (STA)
  Determines which switch has multiple ways to communicate with host
  Determines best path and blocks other paths
Virtual LAN (VLAN) management
  Network may be segmented into logical groups of physical devices through VLAN
  Scattered users may be logically grouped together:
    Regardless of which switch they are attached to
Notes: End of class 10/21/16 10 AM
Network Design Management
Loop protection can prevent broadcast storms
  Uses IEEE 802.1d spanning tree algorithm (STA)
  Determines which switch has multiple ways to communicate with host
  Determines best path and blocks other paths
Virtual LAN (VLAN) management
  Network may be segmented into logical groups of physical devices through VLAN
  Scattered users may be logically grouped together:
    Regardless of which switch they are attached to

## Slide 38: Network Design Management
General principles for managing VLANs
  Configure empty switch ports to connect to an unused VLAN
  Change any default VLAN names
  Configure the ports on the switches that pass tagged VLAN packets to explicitly forward specific tags
  Configure VLANs so that public devices are not on a private VLAN
Notes: Network Design Management
General principles for managing VLANs
  Configure empty switch ports to connect to an unused VLAN
  Change any default VLAN names
  Configure the ports on the switches that pass tagged VLAN packets to explicitly forward specific tags
  Configure VLANs so that public devices are not on a private VLAN

## Slide 39: Port Security
Disabling unused interfaces
  Turn off ports on a network device that are not required
  A switch or router without port security allows attackers to connect to unused ports and attack the network
  All interfaces should be secured before switch is deployed
  The network administrator should issue shutdown command to each unused port
Notes: Port Security
Disabling unused interfaces
  Turn off ports not required on a network device that are not required
  A switch or router without port security allows attackers to connect to unused ports and attack the network
  All interfaces should be secured before switch is deployed
  The network administrator should issue shutdown command to each unused port

## Slide 40: Port Security
MAC limiting and filtering
  Filters and limits the number of media access control (MAC) addresses allowed on a single port
  Port can be set to limit of 1
  Specific MAC address can be assigned to a port
    Enables only single authorized host to connect
Notes: Port Security
MAC limiting and filtering
  Filters and limits the number of media access control (MAC) addresses allowed on a single port
  Port can be set to limit of 1
  Specific MAC address can be assigned to a port
    Enables only single authorized host to connect

## Slide 41: Port Security
Notes: Port Security
Table 8-6 MAC limiting and filtering configuration options

## Slide 42: Port Security
IEEE 802.1x
  Standard that provides the highest degree of port security
  Implements port-based authentication
  Blocks all traffic on a port-by-port basis:
    Until client is authenticated
Notes: Port Security
IEEE 802.1x
  Standard that provides the highest degree of port security
  Implements port-based authentication
  Blocks all traffic on a port-by-port basis:
    Until client is authenticated

## Slide 43: Port Security
Notes: Port Security
Figure 8-8 IEEE 802.1x process

## Slide 44: Securing Network Applications and Platforms
Several network applications and platforms require special security considerations:
  IP telephony
  Virtualization
  Cloud computing
Notes: Securing Network Applications and Platforms
Several network applications and platforms require special security considerations:
  IP telephony
  Virtualization
  Cloud computing

## Slide 45: IP Telephony
A shift to an all digital technology infrastructure is underway
  Converges voice and data traffic over a single IP network
  IP telephony adds digital voice clients and new voice applications to a data based network
An IP telephony application can be easily developed that personalizes the treatment of incoming calls
  Calls can be selectively forwarded or blocked
Notes: IP Telephony
A shift to an all digital technology infrastructure is underway
  Converges voice and data traffic over a single IP network
  IP telephony adds digital voice clients and new voice applications to a data based network
An IP telephony application can be easily developed that personalizes the treatment of incoming calls
  Calls can be selectively forwarded or blocked

## Slide 46: IP Telephony
IP telephony advantages
  Cost savings
  Simplified management
  Application development
  Reduced infrastructure requirements
  Reduced regulatory requirements
  Increased user productivity
Notes: IP Telephony
IP telephony advantages
  Cost savings
  Simplified management
  Application development
  Reduced infrastructure requirements
  Reduced regulatory requirements
  Increased user productivity

## Slide 47: IP Telephony
Notes: IP Telephony
Table 8-7 IP technology vulnerabilities

## Slide 48: Virtualization
Virtualization
  A means of managing and presenting computer resources without regard to physical layout or location
Host virtualization
  An entire operating system environment is simulated
  Virtual machine - a simulated software-based emulation of a computer
  The host system runs a hypervisor that manages the virtual operating systems and supports one or more guest systems
Notes: Virtualization
Virtualization
  A means of managing and presenting computer resources without regard to physical layout or location
Host virtualization
  An entire operating system environment is simulated
  Virtual machine - a simulated software-based emulation of a computer
  The host system runs a hypervisor that manages the virtual operating systems and supports one or more guest systems

## Slide 49: Virtualization
Virtualization advantages
  New virtual server machines can be made available (host availability) and resources can easily be expanded or contracted as needed (host elasticity)
  Can reduce costs
    Fewer physical computers must be purchased and maintained
  Can provided uninterrupted server access to users
    Supports live migration which allows a virtual machine to be moved to a different physical computer with no impact to users
Notes: Virtualization
Virtualization advantages
  New virtual server machines can be made available (host availability) and resources can easily be expanded or contracted as needed (host elasticity)
  Can reduce costs
    Fewer physical computers must be purchased and maintained
  Can provided uninterrupted server access to users
    Supports live migration which allows a virtual machine to be moved to a different physical computer with no impact to users

## Slide 50: Virtualization
Virtualization advantages (cont’d.)
  Test latest patches by downloading on a virtual machine before installing on production computers
  A snapshot of a particular state of a virtual machine can be saved for later use
  Testing the existing security configuration (security control testing) can be performed using a simulated network environment
  A suspicious program can be loaded into an isolated virtual machine and executed (sandboxing)
    If malware, only the virtual machine will be impacted
Notes: End of class 3/6/17
Virtualization
Virtualization advantages (cont’d.)
  Test latest patches by downloading on a virtual machine before installing on production computers
  A snapshot of a particular state of a virtual machine can be saved for later use
  Testing the existing security configuration (security control testing) can be performed using a simulated network environment
  A suspicious program can be loaded into an isolated virtual machine and executed (sandboxing)
    If malware, only the virtual machine will be impacted

## Slide 51: Virtualization
Security for virtualized environments:
  A guest OS that has remained dormant may not contain the latest patches and security updates
  Not all hypervisors have the necessary security controls to keep out attackers
  Existing security tools were designed for single physical servers and do not always adapt well to multiple virtual machines
  Virtual machines must be protected from outside network and other virtual machines on the same computer
Notes: Virtualization
Security for virtualized environments:
  A guest OS that has remained dormant may not contain the latest patches and security updates
  Not all hypervisors have the necessary security controls to keep out attackers
  Existing security tools were designed for single physical servers and do not always adapt well to multiple virtual machines
  Virtual machines must be protected from outside network and other virtual machines on the same computer

## Slide 52: Cloud Computing
Cloud computing
  A model for enabling convenient, on-demand network access to a shared pool of configurable computing resources
  It is a pay-per-use computing model
    Customers pay for only the resources they need
Types of clouds
  Public cloud
  Community cloud
  Private cloud
  Hybrid cloud
Notes: Cloud Computing
Cloud computing
  A model for enabling convenient, on-demand network access to a shared pool of configurable computing resources
  It is a pay-per-use computing model
    Customers pay for only the resources they need
Types of clouds
  Public cloud
  Community cloud
  Private cloud
  Hybrid cloud

## Slide 53: Cloud Computing
Three service models of cloud computing
  Software as a Service (SaaS)
    Vendor provides access to software applications running on a cloud infrastructure
  Platform as a Service (PaaS)
    Consumers install and run their own specialized apps on cloud computing network
  Infrastructure as a Service (IaaS)
    Vendor allows customers to deploy and run their own software, including OSs and applications
Notes: Cloud Computing
Three service models of cloud computing
  Software as a Service (SaaS)
    Vendor provides access to the vendor’s software applications running on a cloud infrastructure
  Platform as a Service (PaaS)
    Consumers install and run their own specialized applications on the cloud computing network
  Infrastructure as a Service (IaaS)
    Vendor allows customers to deploy and run their own software, including OSs and applications

## Slide 54: Cloud Computing
Notes: Cloud Computing
Table 8-8 Cloud computing characteristics

## Slide 55: Cloud Computing
Cloud computing security challenges
  Cloud provider must guarantee means to approve authorized users and deny imposters
  Transmissions from the cloud must be protected
  Customers’ data must be isolated from other customers
  The highest level of application availability and security must be maintained
Notes: Cloud Computing
Cloud computing security challenges
  Cloud provider must guarantee means to approve authorized users and deny imposters
  Transmissions from the cloud must be protected
  Customers’ data must be isolated from other customers
  The highest level of application availability and security must be maintained