## Slide 1: Types of Mobile Devices
Characteristics of mobile devices:
  Small form factor
  Wireless data NIC for accessing the Internet
  Mobile OS
  Apps acquired through different means,
    downloaded from the Web
    provided by the wireless data carrier
  Data synchronization possible with separate computer or remote servers
  Local non-removable data storage
Notes: Types of Mobile Devices
Characteristics of mobile devices:
  Small form factor
  Wireless data NIC for accessing the Internet
  Mobile OS
  Apps that can be acquired through different means, such as downloaded from the Web or provided by the wireless data carrier
  Data synchronization capabilities with a separate computer or remote servers
  Local nonremovable data storage

## Slide 2: Types of Mobile Devices
Optional features that may be found on mobile devices:
  Digital camera(s)
  Global Positioning System (GPS)
  Microphone
  Removable storage media
  Support for using the device as removable storage for another computing device
  Wireless cellular connection
  Wireless personal area network interfaces like Bluetooth or NFC
Notes: Types of Mobile Devices
Optional features that may be found on mobile devices:
  Digital camera(s)
  Global Positioning System (GPS)
  Microphone
  Removable storage media
  Support for using the device itself as removable storage for another computing device
  Wireless cellular connection
  Wireless personal area network interfaces like Bluetooth or near field communications

## Slide 3: Portable Computers
Portable computers
  Similar hardware and the same OS/application software found on a desktop computers
Primary difference
  Smaller self-contained devices
  easily transported from one location to another
  while operating on battery power
Laptop
  Regarded as the earliest portable computer
  Multiple hardware ports and may accommodate limited hardware upgrades
Notes: Portable Computers
Portable computers
  Have similar hardware and run the same OS and application software found on a desktop computer
Primary difference
  Portable computers are smaller self-contained devices that can easily be transported from one location to another while operating on battery power
Laptop
  Regarded as the earliest portable computer
  Have multiple hardware ports and may accommodate limited hardware upgrades

## Slide 4: Portable Computers
Notebook computers
  Smaller version of a laptop computer
  Typically lighter than laptops
  Small enough to fit inside a briefcase
  Include only basic, frequently used features
  Limited number of hardware ports
    Do not include optical drives
  Often cannot be upgraded
Notes: Portable Computers
Notebook computers
  A smaller version of a laptop computer
  Typically weigh less than laptops and are small enough to fit inside a briefcase
  Designed to include only basic, frequently used features
  Have a limited number of hardware ports
    Do not include optical drives
  Often cannot be upgraded

## Slide 5: Portable Computers
Notes: Portable Computers
Table 10-1 Laptop vs. notebook computers

## Slide 6: Portable Computers
Subnotebook computers
  Sometimes called an ultrabook (Intel/Windows) or air (Apple)
  Smaller than notebooks
    low-power processors
    solid state drives (SSDs)
  HDMI port
  limited number of USB hardware ports
Notes: 10 AM 10/31 11 AM
Portable Computers
Subnotebook computers
  Sometimes called an ultrabook (Intel/Windows) or air (Apple)
  Smaller than notebooks and use low-power processors and solid state drives (SSDs)
  Generally have a high-definition multimedia interface (HDMI) port and a limited number of USB hardware ports

## Slide 7: Portable Computers
Web-based computer
  Contains a limited version of the Linux OS and a web browser
  Has an integrated media player
  Designed to be used primarily while connected to the Internet
  No traditional applications can be installed
  No user files stored locally
  Accesses web apps and saves user files on the Internet
Notes: Portable Computers
Web-based computer
  Contains a limited version of the Linux OS and a web browser
  Has an integrated media player
  Designed to be used primarily while connected to the Internet
  No traditional applications can be installed
  No user files are stored locally
  Accesses web apps and saves user files on the Internet

## Slide 8: Tablets
Tablets
  Generally larger than smartphones and smaller than notebooks
  Typically no built-in keyboard
  Rely on a touch screen
  Primary display device with limited user input
  Most popular OSs for tablets are Apple iOS, Google Android, and Microsoft Windows
Notes: Tablets
Tablets
  Portable computing devices generally larger than smartphones and smaller than notebooks
  Generally lack a built-in keyboard
  Rely on a touch screen
  Primary display device with limited user input
  Most popular OSs for tablets are Apple iOS, Google Android, and Microsoft Windows

## Slide 9: Smartphones
Smartphone
  Has all the tools that a feature phone has
  Also includes an OS!
    allows it to run apps and access the Internet
  Considered handheld personal computers
    Because of their ability to run apps
  Vs A feature phone:
    traditional cellular phone with limited features,
      camera, MP3 music player, ability to send and receive short message service (SMS) text messages
Notes: Smartphones
Smartphone
  Has all the tools that a feature phone has but also includes an OS that allows it to run apps and access the Internet
  A feature phone is a traditional cellular phone with limited features, such as camera, MP3 music player, and the ability to send and receive short message service (SMS) text messages
  Considered handheld personal computers
    Because of their ability to run apps

## Slide 10: Smartphones
Notes: Smartphones
Table 10-2 Smartphone vs. feature phone worldwide market share

## Slide 11: Wearable Technology
Wearable technology
  Devices that can be worn by the user instead of carried
Examples of wearable technology:
  Optical head-mounted display
    “Google Glass” can be activated in response to a user’s voice commands
  Smart watch
    Can serve as an accessory to a smartphone to view messages
Notes: Wearable Technology
Wearable technology
  Devices that can be worn by the user instead of carried
Examples of wearable technology:
  Optical head-mounted display
    “Google Glass” can be activated in response to a user’s voice commands
  Smart watch
    Can serve as an accessory to a smartphone to view messages

## Slide 12: Wearable Technology
Notes: Wearable Technology
Figure 10-3 Google Glass

## Slide 13: Legacy Devices
Several mobile devices are no longer widely in use
Personal digital assistant (PDA)
  Intended to replace paper systems
  Often included:
    an appointment calendar, address book, “to-do” list, calculator, and notepad
  Replaced by smartphones
Netbook
  Small, inexpensive, and lightweight computer
  Small screen
  Could not be upgraded
  Lost popularity with introduction of tablet computers
Notes: Legacy Devices
Several mobile devices are no longer widely in use
Personal digital assistant (PDA)
  Intended to replace paper systems
  Often included an appointment calendar, address book, “to-do” list, calculator, and notepad
  Fell out of favor as smartphones gained in popularity
Netbook
  A small, inexpensive, and lightweight computer
  Featured small screens and could not be upgraded
  Lost popularity with introduction of tablet computers

## Slide 14: Mobile Device Removable Storage
Mobile devices
  Use flash memory for permanent storage
  Can be electrically erased and reused
  Most devices also support removable data storage, which includes:
    Large form factor and small form factor storage
Large Form Factor Storage
  Credit card-sized slides into a slot on computer
  Originally known as PCMCIA cards and later name was changed to PC Card
Notes: Mobile Device Removable Storage
Mobile devices
  Use flash memory for storage
  Can be electrically erased and reused
  Most devices also support removable data storage, which includes:
    Large form factor and small form factor storage
Large Form Factor Storage
  A credit card-sized peripheral that slides into a slot on a laptop computer
  Originally known as PCMCIA cards and later name was changed to PC Card

## Slide 15: Mobile Device Removable Storage
The PC Card standard defines three form factors for three types of PC Cards
  Cards differ only in their thickness
  See Table 10-3 for comparisons of the three types
CardBus
  Enhanced type of PC Card includes a bus mastering feature
Being replaced by ExpressCard technology
  Higher-performance expansion in a smaller size
Notes: Mobile Device Removable Storage
The PC Card standard defines three form factors for three types of PC Cards
  Cards differ only in their thickness
  See Table 10-3 for comparisons of the three types
CardBus
  An enhanced type of PC Card that includes a bus mastering feature
PC Card and CardBus are being replaced by ExpressCard technology
  Delivers higher-performance modular expansion in a smaller size

## Slide 16: Mobile Device Removable Storage
Small Form Factor Storage
  CompactFlash(CF) generally used as a mass storage device
  Secure Digital (SD) card includes four card “families” available in three different form factors with different speed ratings
    Standard-Capacity (SDSC)
    High-Capacity (SDHC)
    eXtended-Capacity (SDXC)
    Secure Digital Input Output (SDIO)
Notes: Mobile Device Removable Storage
Small Form Factor Storage
  CompactFlash(CF) generally used as a mass storage device
  Secure Digital (SD) card includes four card “families” available in three different form factors with different speed ratings
    Standard-Capacity (SDSC)
    High-Capacity (SDHC)
    eXtended-Capacity (SDXC)
    Secure Digital Input Output (SDIO)

## Slide 17: Mobile Device Removable Storage
Three sizes of SD cards:
  Full SD - typically used in PCs, video cameras, digital cameras, other large electronic devices
  miniSD and microSD - commonly used in smaller devices like smartphones and tablets
SD speed classes were designed to support video recording
There are two types of speed classes:
  Standard and ultra high speed (UHS)
Notes: Mobile Device Removable Storage
Three sizes of SD cards:
  Full SD - typically used in PCs, video cameras, digital cameras, other large electronic devices
  miniSD and microSD - commonly used in smaller devices like smartphones and tablets
SD speed classes were designed to support video recording
There are two types of speed classes:
  Standard and ultra high speed (UHS)

## Slide 18: Mobile Device Risks
Mobile device security risks:
  Limited physical security
  Connecting to public networks
  Location tracking
  Installing unsecured applications
  Accessing untrusted content
  Bring your own device (BYOD) risks
Notes: Mobile Device Risks
Mobile device security risks:
  Limited physical security
  Connecting to public networks
  Location tracking
  Installing unsecured applications
  Accessing untrusted content
  Bring your own device (BYOD) risks

## Slide 19: Limited Physical Security
A mobile device is stolen on average once every 50 seconds
One-third of all laptops stolen in the U.S. go missing from public schools
Consumer-owned laptops are most often in August and September and November and December
Laptop theft is prevalent at airports
Users must guard against shoulder surfing
  Strangers who want to view sensitive information
Notes: Limited Physical Security
A mobile device is stolen on average once every 50 seconds
One-third of all laptops stolen in the U.S. go missing from public schools
Consumer-owned laptops are most often in August and September and November and December
Laptop theft is prevalent at airports
Users must guard against shoulder surfing
  Strangers who want to view sensitive information

## Slide 20: Limited Physical Security
Notes: Limited Physical Security
Table 10-5 Top five areas for airport laptop theft

## Slide 21: Connecting to Public Networks
Many mobile devices use public external networks for Internet access
Attackers can eavesdrop on the data transmissions and view sensitive information
Open networks may be susceptible to man-in-the-middle or replay attacks
Notes: Connecting to Public Networks
Many mobile devices use public external networks for Internet access
Attackers can eavesdrop on the data transmissions and view sensitive information
Open networks may be susceptible to man-in-the-middle or replay attacks

## Slide 22: Location Tracking
Location services
  Can identify the location of a person carrying a mobile device
  Used extensively by social media, navigation systems, weather systems, and other mobile-aware applications
Mobile devices using location services are at risk of targeted physical attacks
  Attacker can follow user in order to steal the device or inflict harm upon the person
Notes: Location Tracking
Location services
  Can identify the location of a person carrying a mobile device
  Used extensively by social media, navigation systems, weather systems, and other mobile-aware applications
Mobile devices using location services are at risk of targeted physical attacks
  Attacker can follow user in order to steal the device or inflict harm upon the person

## Slide 23: Installing Unsecured Applications
Mobile devices are designed to easily locate, acquire, and install apps from a variety of sources
Many apps do not include security features
Mobile OSs have different levels of security
Apple iOS
  A closed and proprietary architecture
  More difficult for attackers to create an app that could compromise it
  Uses its App Store as the sole source for distributing apps
Notes: Installing Unsecured Applications
Mobile devices are designed to easily locate, acquire, and install apps from a variety of sources
Many apps do not include security features
Mobile OSs have different levels of security
Apple iOS
  A closed and proprietary architecture
  More difficult for attackers to create an app that could compromise it
  Uses its App Store as the sole source for distributing apps

## Slide 24: Installing Unsecured Applications
Apple iOS (cont’d)
  A recent study compared the top 200 iOS and Android apps
    Found that iOS apps exhibited a greater percentage of risky behaviors than Android apps
Notes: Installing Unsecured Applications
Apple iOS (cont’d)
  A recent study compared the top 200 iOS and Android apps
    Found that iOS apps exhibited a greater percentage of risky behaviors than Android apps
Table 10-6 Apple iOS apps risky behavior

## Slide 25: Installing Unsecured Applications
Google Android
  Not proprietary and open for anyone to use or modify
  Apps downloaded from Google Play store or from unofficial third-party websites
  This makes Android apps highly risky
  Most malicious apps designed to trick users into downloading costly services or steal user data
Notes: 11/2 1PM
Installing Unsecured Applications
Google Android
  Not proprietary and open for anyone to use or modify
  Apps can be downloaded from the Google Play store or from an unofficial third-party website (sideloading)
  This makes Android apps highly risky
  Most malicious apps are designed to trick users into downloading costly services or may steal user data

## Slide 26: Accessing Untrusted Content
Quick Response (QR) codes
  A matrix or two-dimensional barcode
    can be read by an imaging device
  Applications for these codes include:
    Product tracking, item identification, time tracking, document management, and general marketing
  Attacker can create an ad listing a reputable website but QR code that contains a malicious URL
    Code directs a user’s browser to attacker’s website or a site that downloads malware
Notes: End of class 10 AM 3/15/17
Accessing Untrusted Content
Quick Response (QR) codes
  A matrix or two-dimensional barcode which can be read by an imaging device
  Applications for these codes include:
    Product tracking, item identification, time tracking, document management, and general marketing
  An attacker can create an advertisement listing a reputable website but include a QR code that contains a malicious URL
    Code directs a user’s browser to the attacker’s imposter website or to a site that downloads malware

## Slide 27: Bring Your Own Device (BYOD) Risks
Bring Your Own Device (BYOD) policy
  Allows users to use own mobile device for business or organizational purposes
Risks associated with BYOD:
  Users may erase the installed/built-in limitations on their smartphone
  Often shared with family members and friends
  Technical support staff has to support hundreds of different mobile devices
  If an employee is let go, difficult to erase any corporate data from personal mobile device
Notes: End of class 11 AM 11/2
Bring Your Own Device (BYOD) Risks
Bring Your Own Device (BYOD) policy
  Allows users to use their own personal mobile device for business or organizational purposes
Risks associated with BYOD:
  Users may erase the installed built-in limitations on their smartphone
  Often shared with family members and friends
  Technical support staff may have to support hundreds of different mobile devices
  If an employee is let go, it may be difficult to erase any corporate data from personal mobile device

## Slide 28: Securing Mobile Devices
Steps to securing mobile devices:
  Initial setup of the device
  Its ongoing management
  Deal with theft or loss of the device
Notes: Securing Mobile Devices
Steps to securing mobile devices:
  Initial setup of the device
  Its ongoing management
  Deal with theft or loss of the device

## Slide 29: Device Setup
Disable Unused Features
  Disable unused features and turn off those that do not support the business use of the phone
  Disable Bluetooth wireless data communication
    In order to prevent bluejacking and bluesnarfing
Enable Lock Screen after inactivity
  Prevents device from being used until the user enters the correct passcode
Notes: Device Setup
Disable Unused Features
  It is important to disable unused features and turn off those that do not support the business use of the phone
  Should disable Bluetooth wireless data communication
    In order to prevent bluejacking and bluesnarfing
Enable Lock Screen
  Lock screen prevents device from being used until the user enters the correct passcode
    Set screen to lock after a period of inactivity

## Slide 30: Device Setup
Enable Lock Screen (cont’d)
  After a number of failed attempts to enter passcode, additional security protections will occur:
    Extend lockout period
    Reset to factory settings
  Most devices have options for the type of passcode
    A popular option is to draw or swipe a specific pattern connecting dots
    Least effective code is a short PIN
Notes: Device Setup
Enable Lock Screen (cont’d)
  After a specific number of failed attempts to enter a passcode, additional security protections will occur:
    Extend lockout period
    Reset to factory settings
  Most devices have different options for the type of passcode
    A popular option is to draw or swipe a specific pattern connecting dots
    Least effective code is a short PIN

## Slide 31: Device Setup
Notes: Device Setup
Table 10-7 Most Common PINs

## Slide 32: Device Setup
Use Encryption
  Neither iOS or Android provide native cryptography,
    third-party apps must be installed to provide encryption
  Two encryption options:
    Full device encryption
    Separating data storage into containers and encrypt only sensitive data
Notes: Device Setup
Use Encryption
  Neither iOS or Android provide native cryptography, so third-party apps must be installed to provide encryption
  Two encryption options:
    Full device encryption
    Separating data storage into containers and encrypt only the sensitive data

## Slide 33: Device Setup
Control Access
  A key to securing mobile devices
    reduce access to the device and its data by
    limiting who is authorized to use the information
  At a higher corporate level decisions must be made on who can access the data before it is downloaded onto a mobile device
  Many organizations are beginning to focus their efforts on the data instead of just the device by extending data loss prevention to mobile devices
Notes: End of class 11/2/16 10 AM
Control Access
  A key to securing mobile devices is to control access to the device and its data by limiting who is authorized to use the information
  At a higher corporate level decisions must be made on who can access the data before it is downloaded onto a mobile device
  Many organizations are beginning to focus their efforts on the data instead of just the device by extending data loss prevention to mobile devices

## Slide 34: Device and App Management
Mobile Device Management (MDM)
  Tools that allow a device to be managed remotely by an organization
  Usually involve:
    A server component that sends out management commands to mobile devices
    A client component to receive and implement the management commands
  An administrator can perform over the air (OTA) updates or configuration changes to one device
Notes: Device and App Management
Mobile Device Management (MDM)
  Tools that allow a device to be managed remotely by an organization
  Usually involve:
    A server component that sends out management commands to mobile devices
    A client component to receive and implement the management commands
  An administrator can perform over the air (OTA) updates or configuration changes to one device

## Slide 35: Device and App Management
Some features that MDM tools provide:
  Rapidly enroll new mobile devices (on-boarding) and quickly remove devices (off-boarding)
  Apply or modify default device settings
  Enforce encryption settings, antivirus updates, and patch management
  Display an acceptable use policy that requires consent before allowing access
  Configure email, calendar, contacts, Wi-Fi, and VPN profiles OTA
  Discover devices accessing enterprise systems
Notes: Device and App Management
Some features that MDM tools provide:
  Rapidly enroll new mobile devices (on-boarding) and quickly remove devices (off-boarding)
  Apply or modify default device settings
  Enforce encryption settings, antivirus updates, and patch management
  Display an acceptable use policy that requires consent before allowing access
  Configure email, calendar, contacts, Wi-Fi, and VPN profiles OTA
  Discover devices accessing enterprise systems

## Slide 36: Device and App Management
Some features that MDM tools provide (cont’d):
  Approve or quarantine new mobile devices
  Distribute and manage public and corporate apps
  Securely share and update documents and corporate policies
  Detect and restrict jailbroken and rooted devices
  Selectively erase corporate data
  Facilitate asset tracking and inventory control
Notes: Device and App Management
Some features that MDM tools provide (cont’d):
  Approve or quarantine new mobile devices
  Distribute and manage public and corporate apps
  Securely share and update documents and corporate policies
  Detect and restrict jailbroken and rotted devices
  Selectively erase corporate data
  Facilitate asset tracking and inventory control

## Slide 37: Device and App Management
Mobile Application Management (MAM)
  Also called application control
  Tools and services responsible for distributing and controlling access to apps
  Initially controlled apps through app wrapping
    Sets up a “dynamic” library of software routines and adds to an existing program to restrict parts of an app
  Using a MAM originally required the use of an MDM as well
  Newer versions of mobile OSs have MAM incorporated into the software itself
Notes: Device and App Management
Mobile Application Management (MAM)
  Also called application control
  Tools and services responsible for distributing and controlling access to apps
  Initially controlled apps through app wrapping
    Sets up a “dynamic” library of software routines and adds to an existing program to restrict parts of an app
  Using a MAM originally required the use of an MDM as well
  Newer versions of mobile OSs have MAM incorporated into the software itself

## Slide 38: Device Loss or Theft
To reduce the risk of theft or loss:
  Keep the mobile device out of sight when traveling
  Always maintain awareness of your surroundings
  When holding the device, use both hands to make it difficult for a thief to snatch
  Don’t use device on escalators or near train doors
If a device is lost or stolen, it may be necessary to perform a remote wiping, which erases sensitive data stored on the device
Notes: Device Loss or Theft
To reduce the risk of theft or loss:
  Keep the mobile device out of sight when traveling in a high-risk area
  Always maintain awareness of your surroundings
  When holding the device, use both hands to make it difficult for a thief to snatch
  Do not use the device on escalators or near train doors
If a device is lost or stolen, it may be necessary to perform a remote wiping, which erases sensitive data stored on the device

## Slide 39: Device Loss or Theft
Notes: Device Loss or Theft
Table 10-8 Security features for locating lost or stolen mobile devices

## Slide 40: Mobile Device App Security
Apps on the device should be secured also
Apps can require that the user provide authentication (such as a passcode) before access is granted
MDMs can support:
  Application whitelisting - ensures that only preapproved apps can run on the device
  Geo-fencing - uses the device’s GPS to define geographical boundaries where the app can be used
  Credential management - stores authentication information
Notes: Mobile Device App Security
Apps on the device should be secured also
Apps can require that the user provide authentication (such as a passcode) before access is granted
MDMs can support:
  Application whitelisting - ensures that only preapproved apps can run on the device
  Geo-fencing - uses the device’s GPS to define geographical boundaries where the app can be used
  Credential management - stores authentication information

## Slide 41: BYOD Security
Benefits of BYOD for companies:
  Management flexibility
  Less oversight
  Cost savings
  Increased employee performance
  Simplified IT infrastructure
  Reduced internal service
MDMs and MAMs are important in managing BYOD devices
Notes: BYOD Security
Benefits of BYOD for companies:
  Management flexibility
  Less oversight
  Cost savings
  Increased employee performance
  Simplified IT infrastructure
  Reduced internal service
MDMs and MAMs are important in managing BYOD devices